Characterization Of Rock Fracture by Digital Image Analysis

## Afdal1) and U. Fauzi2)

1) Department of Physics, Andalas University

Kampus Unand, Limau Manis, Padang, 25163

e-mail: aafdal@yahoo.com

2) Department of Physics, Bandung Institute of Technology

#### Jl. Ganesha No. 10, Bandung, 40132

## Abstract

Fractures play an important role and determine behavior of fluid flow through porous media, such as oil, gas, and geothermal reservoirs. Identification of  fracture characteristics that affect physical properties of rock become important. Characterization of rock fracture can be conducted using digital image analysis method. This method gives quantitative characterization of rock fracture. Fracture characteristics investigated in this research are length, width, orientation, distribution, density, intensity, and fractal dimension. Fractal dimension is calculated by box-counting method.

In this study, characterization was performed on digital image of rock samples and outcrop walls fracture pattern that are collected from Lembang fault, in West Java. It is observed that dimension of both rock samples and outcrop walls are fractal. Fractal dimension for these two groups show similar value. Fractal dimension of outcrop walls are larger than that of rock samples. Fractal dimension of rock samples range from 1.10 to 1.13 and fractal dimension of outcrop wall varies from 1,13 to 1,17. The data also show that fractal dimension is in direct relation with fracture density.

Key words: characterization, digital image, fractal dimension, fracture.

## Abstrak

Rekahan mempunyai peranan penting dan menentukan kelakuan aliran fluida dalam media berpori seperti sumur minyak, gas, dan geothermal. Mengetahui karakteristik rekahan yang mempengaruhi sifat fisik batuan menjadi penting. Karakterisasi rekahan batuan dapat dilakukan dengan analisis citra digital. Metode ini memberikan karakterisasi kuantitatif terhadap rekahan batuan. Karakteristik yang ditentukan disini adalah panjang, lebar, orientasi, distribusi, densitas, intensitas, dan dimensi fraktal. Dimensi fraktal dihitung dengan metode box-counting.

Dalam penulisan ini karakterisasi dilakukan terhadap citra pola rekahan sampel batuan dan dinding singkapan yang diambil di sesar Lembang, Jawa Barat. Hasil menunjukkan bahwa dimensi rekahan batuan dan dinding sigkapan tersebut adalah fraktal. Dimensi fraktal cenderung sama untuk kedua kelompok sampel dan dimensi fraktal sampel dinding singkapan lebih besar daripada dimensi fraktal sampel batuan. Nilai dimensi fraktal sampel batuan berkisar dari 1,10 sampai 1,13, sedangkan  dimensi fraktal sampel dinding singkapan dengan selang 1,13 sampai 1,17. Data juga menunjukkan bahwa dimensi fraktal rekahan batuan berbanding lurus dengan densitas rekahan.

Kata kunci : citra digital, dimensi fraktal, karakterisasi, rekahan.